The goal of this sub study is to align, in Exp- & Sim-Data, distribution of Lorentz Invariant quantities (Q2,W,MM(x) etc). To this end, the following specific subjects are addressed
(which are defined in detail in the document):
Momentum Corrections
Effective Momentum Corrections
GPP parameters

---
Assumptions
1. Event Generator ≡ Nature
2. GSIM ≠ CLAS
a. Distribution of Raw detector quantities, as obtained from GSIM and CLAS, for example Track's Hit position from the DC, may be distributed with different resolutions. Therefore, Track Kinematics and subsequent Lorentz Vectors reconstructed and their Invariants, will also have varying resolutions.
b. CLAS may have misaligned detector elements, leading to systematic errors in reconstructing Track Kinematics and LV Invariants.
Aligning distribution of Invariants to Expected Distribution
(Expected Distribution=Natural Distribution, smeared by CLAS resolution)
Experiment(parameters: MomCorr, EffectiveMomCorr-Exp)
Correct for systematic errors in reconstructing Track Kinematics due to misaligned detector elements(MomCorr)
http://www.jlab.org/Hall-B/secure/e1f/mirazita/momcorr/
If needed, apply EffectiveMomCorr-Exp (in effect, adjust beam energy)
MomCorr(p) = A +Bp + Cp2 (from conversation with Evan) and it appears that, depending on the kinematic region of interest, MomCorr maybe over/under-correcting; “tuning” beam energy(be) in this case, serves to offset this.
2) Simulation(parameters: GPP-PARS, EffectiveMomCorr-Sim)
Simulation parameters are adjusted to match Experimental distributions

---
2. Sim. Parameters: be-sim, gpp-pars
1. Exp. Parameters: be-exp
1. Obtain e',p',π+,π momentum from DC
2. Apply MomCorr to e' momentum
3. Reconstruct Invariants:
MMtop<x>
  - If μ,σ ~ Expected values, keep be-exp, else
    Adjust be-exp (EffectiveMomCorr-Exp)
.
1. Obtain e',p',π+,π momentum from DC
2. N.A.
3. Reconstruct Invariants:
MMtop<x>
  - If μ,σ ~ Experimental values, keep gpp-pars & be-sim, else
    Adjust gpp-pars
    Adjust be-sim (EffectiveMomCorr-Sim)
.
Therefore, after these 2 steps, MM distributions, in Exp- & Sim-Data, should match
each other and their be in accordance with the Expected Distribution

---
Results and Observations for:
[Q2,W] = [1.9,2.5][1.3,1.9]
Double, charged electroproduction (Simulation uses “Model”)
Cuts applied before obtain MM distributions: eid,efid
Experimental Parameters:
be-exp=5.497 GeV
Simulation Parameters:
gpp-pars = 1.37,1.37,1.37 (same as Evan's)
be-sim=5.485 GeV
<Show plots>
MM distributions in Exp- & Sim-Data are not in 100% agreement. What are the repercussions? Systematic errors in Acceptance calculation.
Since SA = SR/ST and SR distribution is narrower/wider compared with Expected Distribution, SA can be over/underestimated. Therefore, EC can be under/over estimated.
  Current estimate of error ≈ -2% to -1% (depending on topology)
ii. Exp- & Sim-Data will have varying levels of Bin Migration and this will be a another	(secondary?) source of systematic error in Acceptance calculation

---
(Related & Unrelated) Future work
Apply pid,hfid etc to clear up Background under MM distributions.
Improve fits to exp-MM distributions and improve error estimation of Acceptance
More importantly, find a better estimate for MM cuts
Study MM cut for Top 1 in more detail
Finish Q2,W resolution study for Simulation and start full kinematic Simulation!