The goal of this sub study is to
1. Align, in Exp- & Sim-Data, distribution of Lorentz Invariant quantities (Q2,W,MM(x) etc). To this end, the following specific subjects are addressed
(which are defined in detail in the document):
Momentum Corrections
Effective Momentum Corrections
GPP parameters
DATADIR and ANADIR:
Sim-DATADIR: /e1f.sim2pi.datadir/setup_sim_CentOS6
Sim-ANADIR: Within respective Sim-DATADIR
Exp-DATADIR: /e1f.2pi.datadir2/./h10/, /e1f.2pi.datadir1/./h10/
Exp-ANADIR: /datadir2/e1f/ana-2pi/exp/q2w2, /datadir2/e1f/ana-2pi/exp/q2w1
Executables used: sub_studies/setup_sim_CentOS6/make_d2pi (for sim-data only)
Scripts used:
scripts/python/ana_tools.py::plot_ana2pi_MMs()
2. Determine Simulation range for my kinematics [2.0,5.0 ][1.3,3.0]

---
mtg-012714
SS.1: Aligning...

---
Assumptions
1. Event Generator ≡ Nature
2. GSIM ≠ CLAS
a. Distribution of Raw detector quantities, as obtained from GSIM and CLAS, for example Track's Hit position from the DC, may be distributed with different resolutions. Therefore, Track Kinematics and subsequent Lorentz Vectors reconstructed and their Invariants, will also have varying resolutions.
b. CLAS may have misaligned detector elements, leading to systematic errors in reconstructing Track Kinematics and LV Invariants.
Aligning distribution of Invariants to Expected Distribution
(Expected Distribution=Natural Distribution, smeared by CLAS resolution)
Experiment(parameters: MomCorr, EffectiveMomCorr-Exp)
Correct for systematic errors in reconstructing Track Kinematics due to misaligned detector elements(MomCorr)
http://www.jlab.org/Hall-B/secure/e1f/mirazita/momcorr/
After this step it is assumed that the distribution of Track Kinematic variables are in	agreement with the Expected Distribution. There may be a systematic offset of the	mean value of the Expected Distribution, for which the following step has to be taken
If needed, apply EffectiveMomCorr-Exp to cancel systematic offset of mean of Expected Distribution. The systematic offset could be due to(in effect, adjust beam energy)
MomCorr(p) = A(p) +B(p)p + C(p)p2 (from conversation with Evan) and it appears that, depending on the kinematic region of interest, MomCorr maybe over/under-correcting; “tuning” beam energy(be) in this case, serves to offset this.
Systematic offsets produced by CLAS electronics, user_ana, etc. (Effects that I have not taken the time to investigate)

---
2) Simulation(parameters: GPP-PARS, EffectiveMomCorr-Sim)
Simulation parameters are adjusted to match Experimental distributions
(cont...)
In Simulation, no MomCor is needed, since detector segments are assumed to be aligned in GSIM's detector geometry.
Because of assumption 2.a., GPP parameters are introduced for “tuning” the distribution of Raw detector quantities as output by GSIM to match that obtained directly from CLAS. While this tuning cannot be observed directly, since such Raw detector quantities are no accessible after Reconstruction, the effects of tuning can be observed by comparing, for example Hit positions and Track Kinematics as Reconstructed by user_ana for exp- & sim-data. As a consequence, the Lorentz Invariant quantities obtained from both datasets, should also be similar.
It is assumed that once tuned, gpp-pars should work for all kinematic ranges
Just as EffectiveMomCorr-Exp compensates for any systematic offsets of the mean of Expected distributions in Exp-Data, a similar EffectiveMomCorr-Sim is used to bring to agreement, any systematic offset of means of Expected Distributions in Sim-Data from Exp-Data.
NOTE: EffectiveMomCorr-Exp/Sim may be momentum dependent! Therefore, for each kinematic range, these parameters may have to be tuned differently! Actually, there is already indication for this, since to align elastic peaks I had used be-exp=5.495GeV and to align MM distributions in q2w2, I used be-exp=5.497 GeV

---
2. Sim. Parameters: be-sim, gpp-pars
1. Exp. Parameters: be-exp
1. Obtain e',p',π+,π momentum from DC
2. Apply MomCorr to e' momentum
3. Reconstruct Invariants:
MMtop<x>
  - If μ,σ ~ Expected values, keep be-exp, else
    Adjust be-exp (EffectiveMomCorr-Exp)
.
1. Obtain e',p',π+,π momentum from DC
2. N.A.
3. Reconstruct Invariants:
MMtop<x>
  - If μ,σ ~ Experimental values, keep gpp-pars & be-sim, else
    Adjust gpp-pars
    Adjust be-sim (EffectiveMomCorr-Sim)
.
Therefore, after these 2 steps, MM distributions, in Exp- & Sim-Data, should match
each other and their be in accordance with the Expected Distribution

---
Results and Observations for:
[Q2,W] = [1.9,2.5][1.3,1.9]
Double, charged electroproduction (Simulation uses “Model”)
Cuts applied before obtain MM distributions: eid,efid
Experimental Parameters:
be-exp=5.497 GeV
Simulation Parameters:
Gpp-pars = 1.37,1.37,1.37,0.962 (same as Evan's)
be-sim=5.485 GeV
<Show plots>
MM distributions in Exp- & Sim-Data are not in 100% agreement. What are the repercussions? Systematic errors in Acceptance calculation.
Since SA = SR/ST and SR distribution is narrower/wider compared with Expected Distribution, SA can be over/underestimated. Therefore, EC can be under/over estimated.
  Current estimate of error ≈ -2% to -1% (depending on topology)
ii. Exp- & Sim-Data will have varying levels of Bin Migration and this will be a another	(secondary?) source of systematic error in Acceptance calculation

---
(Related & Unrelated) Future work
Apply pid,hfid etc to clear up Background under MM distributions.
Improve fits to exp-MM distributions and improve error estimation of Acceptance
More importantly, find a better estimate for MM cuts
Study MM cut for Top 1 in more detail
Finalize cuts for each Topology
For this, BG under MM distributions will have to be understood
Finish Q2,W resolution study for Simulation and start full kinematic Simulation!
I should keep in mind that the EffectiveMomCorr-Exp/Sim that I obtain from q2w2, may not work for my full kinematic region!
General Knowledge gained from in meeting
Techniques for BG subtraction:
Sideband subtraction
Subtract BG using Sim-Data
Estimate BG using Exp-Data and then subtract